## Slide 1: RDMA Deployments: From Cloud Computing to Machine Learning
Chuanxiong Guo
Hot Interconnects 2017
August 29 2017
Microsoft Research

## Slide 2
The Rising of Cloud Computing
40
AZURE REGIONS

## Slide 3: Data Centers

## Slide 4
Data Centers

## Slide 5: Data center networks (DCN)
Cloud scale services: IaaS, PaaS, Search, BigData, Storage, Machine Learning, Deep Learning
Services are latency sensitive or bandwidth hungry or both
Cloud scale services need cloud scale computing and communication infrastructure

## Slide 6: Data center networks (DCN)
Single ownership
Large scale
High bisection bandwidth
Commodity Ethernet switches
TCP/IP protocol suite
Spine
Leaf
ToR
Podset
Pod
Servers

## Slide 7: But TCP/IP is not doing well

## Slide 8: TCP latency
405us (P50)
716us (P90)
2132us (P99)
Long latency tail
Pingmesh measurement results

## Slide 9: TCP processing overhead (40G)
Sender
Receiver
8 tcp connections
40G NIC

## Slide 10: An RDMA renaissance story
Notes: Apparently, TCP has severe latency and CPU overhead issues. RDMA, a technology that has been introduced for around 20 years for high performance computing, finally got its chance.

## Slide 11: RDMA
Remote Direct Memory Access (RDMA): Method of accessing memory on a remote system without interrupting the processing of the CPU(s) on that system
IBVerbs/NetDirect for RDMA programing
RDMA offloads packet processing protocols to the NIC
RDMA in Ethernet based data centers (RoCEv2)

## Slide 12: RoCEv2: RDMA over Commodity Ethernet
RoCEv2 for Ethernet based data centers
RoCEv2 encapsulates packets in UDP
OS kernel is not in data path
NIC for network protocol processing and message DMA
TCP/IP
NIC driver
User
Kernel
Hardware
RDMA transport
IP
Ethernet
RDMA app
DMA
RDMA verbs
TCP/IP
NIC driver
Ethernet
RDMA app
DMA
RDMA verbs
Lossless network
RDMA transport
IP

## Slide 13: RDMA benefit: latency reduction
Msg size | TCP P50 (us) | TCP P99 (us) | RDMA P50 (us) | RDMA P99 (us)
1KB | 236 | 467 | 24 | 40
16KB | 580 | 788 | 51 | 117
128KB | 1483 | 2491 | 247 | 551
1MB | 5290 | 6195 | 1783 | 2214
For small msgs (<32KB), OS processing latency matters
For large msgs (100KB+), speed matters

## Slide 14: RDMA benefit: CPU overhead reduction
Sender
Receiver
One ND connection
40G NIC
37Gb/s goodput

## Slide 15: RDMA benefit: CPU overhead reduction
RDMA: Single QP, 88 Gb/s, 1.7% CPU
TCP: Eight connections, 30-50Gb/s,
Client: 2.6%, Server: 4.3% CPU
Intel(R) Xeon(R) CPU E5-2690 v4 @ 2.60GHz, two sockets 28 cores

## Slide 16: RoCEv2 needs a lossless Ethernet network
PFC for hop-by-hop flow control
DCQCN for connection-level congestion control

## Slide 17: Priority-based flow control (PFC)
Hop-by-hop flow control, with eight priorities for HOL blocking mitigation
The priority in data packets is carried in the VLAN tag
PFC pause frame to inform the upstream to stop
PFC causes HOL and colleterial damage
PFC pause frame
p1
Egress port
Ingress port
p0
p1
p7
Data packet
p0
p0
p1
p7
XOFF threshold
Data packet
PFC pause frame

## Slide 18: DCQCN
CP: Switches use ECN for packet marking
NP: periodically check if ECN-marked packets arrived, if so, notify the sender
RP: adjust sending rate based on NP feedbacks
Sender NIC
Reaction Point
(RP)
Switch
Congestion Point (CP)
Receiver NIC
Notification Point (NP)
DCQCN = Keep PFC + Use ECN + hardware rate-based congestion control

## Slide 19: The deployment, safety, and performance challenges
Issues of VLAN-based PFC
RDMA transport livelock
PFC deadlock
PFC pause frame storm
Slow-receiver symptom

## Slide 20: Issues of VLAN-based PFC
Our data center networks run L3 IP forwarding, no standard way for carrying VLAN tags among the switches in L3 networks
VLAN config breaks PXE boot
TOR Switch
NIC
Trunk mode for VLAN tag
No VLAN tag when PXE boot
PS Service

## Slide 21: Our solution: DSCP-based PFC
DSCP field for carrying the priority value
No change needed for the PFC pause frame
Supported by major switch/NIC venders
PFC pause frame
Data packet

## Slide 22: RDMA transport livelock
RDMA Send 0
RDMA Send 1
RDMA Send N+1
NAK N
RDMA Send 0
RDMA Send 1
RDMA Send 2
RDMA Send N+2
Go-back-0
Go-back-N
RDMA Send 0
RDMA Send 1
RDMA Send N+1
NAK N
RDMA Send N
RDMA Send N+1
RDMA Send N+2
RDMA Send N+2
Sender
Receiver
Switch
Pkt drop rate 1/256
Sender
Receiver
Receiver
Sender

## Slide 23: PFC deadlock
Our data centers use Clos network
Packets first travel up then go down
No cyclic buffer dependency for up-down routing -> no deadlock
But we did experience deadlock!
Spine
Leaf
ToR
Podset
Pod
Servers

## Slide 24: PFC deadlock
Preliminaries
  ARP table: IP address to MAC address mapping
  MAC table: MAC address to port mapping
  If MAC entry is missing, packets are flooded to all ports
IP | MAC | TTL
IP0 | MAC0 | 2h
IP1 | MAC1 | 1h
MAC | Port | TTL
MAC0 | Port0 | 10min
MAC1 | - | -
Input
Output
Dst: IP1
ARP table
MAC table

## Slide 25: PFC deadlock
La
Lb
T0
T1
S1
S2
S3
S4
Server
p0
p1
p2
p3
p0
p1
p3
p4
p0
p1
p0
p1
Egress
port
Ingress
port
1
4
3
2
PFC pause frames
p2
S5
Packet drop
Congested port
Dead server
PFC pause frames
Path: {S1, T0, La, T1, S3}
Path: {S1, T0, La, T1, S5}
Path: {S4, T1, Lb, T0, S2}

## Slide 26: PFC deadlock
The PFC deadlock root cause: the interaction between the PFC flow control and the Ethernet packet flooding
Solution: drop the lossless packets if the ARP entry is incomplete
Recommendation: do not flood or multicast for lossless traffic

## Slide 27: Tagger: practical PFC deadlock prevention
L0
T0
L1
S0
S1
L2
T2
L3
T1
T3
L0
T0
L1
S0
S1
L2
T2
L3
T1
T3
Tagger Algorithm works for general network topology
Deployable in existing switching ASICs
Concept: Expected Lossless Path (ELP) to decouple Tagger from routing
Strategy: move packets to different lossless queue before CBD forming with pre-calculated rules

## Slide 28: NIC PFC pause frame storm
A malfunctioning NIC may block the whole network
PFC pause frame storms caused several incidents
Solution: watchdogs at both NIC and switch sides to stop the storm
ToRs
Leaf layer
Spine layer
servers
0
1
2
3
4
5
6
7
Malfunctioning NIC
Podset 0
Podset 1

## Slide 29: The slow-receiver symptom
ToR to NIC is 40Gb/s, NIC to server is 64Gb/s
But NICs may generate large number of PFC pause frames
Root cause: NIC is resource constrained
Mitigation
  Large page size for the MTT (memory translation table) entry
  Dynamic buffer sharing at the ToR
CPU
DRAM
ToR
QSFP
40Gb/s
PCIe
Gen3 8x8 64Gb/s
MTT
WQEs
QPC
NIC
Server
Pause frames

## Slide 30: Deployment experiences and lessons learned

## Slide 31: Latency reduction
RoCEv2 deployed in Bing world-wide for two and half years
Significant latency reduction
Incast problem solved as no packet drops

## Slide 32: RDMA throughput
Using two podsets each with 500+ servers
5Tb/s capacity between the two podsets
Achieved 3Tb/s inter-podset throughput
Bottlenecked by ECMP routing
Close to 0 CPU overhead

## Slide 33: Latency and throughput tradeoff
L0
T0
L1
T1
L1
L1
S0,0
S0,23
S1,0
S1,23
RDMA latencies increase as data shuffling started
Low latency vs high throughput
us
Before data shuffling
During data shuffling

## Slide 34: Lessons learned
Providing lossless is hard!
Deadlock, livelock, PFC pause frames propagation and storm did happen
Be prepared for the unexpected
  Configuration management, latency/availability, PFC pause frame, RDMA traffic monitoring
NICs are the key to make RoCEv2 work

## Slide 35: What’s next?

## Slide 36
Applications
Technologies
Architectures
Protocols
RDMA for X (Search, Storage, HFT, DNN, etc.)
Lossy vs lossless network
Practical, large-scale deadlock free network
RDMA programming
RDMA for heterogenous computing systems
RDMA virtualization
Reducing colleterial damage
RDMA security
Software vs hardware
Inter-DC RDMA

## Slide 37: Will software win (again)?
Historically, software based packet processing won (multiple times)
  TCP processing overhead analysis by David Clark, et al.
  None of the stateful TCP offloading took off (e.g., TCP Chimney)
The story is different this time
  Moore’s law is ending
  Accelerators are coming
  Network speed keep increasing
  Demands for ultra low latency are real

## Slide 38: Is lossless mandatory for RDMA?
There is no binding between RDMA and lossless network
But implementing more sophisticated transport protocol in hardware is a challenge

## Slide 39: RDMA virtualization for the container networking
A router acts as a proxy for the containers
Shared memory for improved performance
Zero copy possible

## Slide 40: RDMA for DNN
Distributed DNN training iterations
  Forward propagation
  Back propagation
  Update gradients
Computation
Communication

## Slide 41: RDMA for DNN
Compute
Communication
Minibatch1
Epoch0
Epoch1
Epoch2
Epoch3
Epoch M
Minibatch0
Minibatch2
Minibatch N
GPU0
Compute
Communication
GPU1
Compute
Communication
GPU X
Data transmission
Training

## Slide 42: RDMA Programming
How many LOC for a “hello world” communication using RDMA?
For TCP, it is 60 LOC for client or server code
For RDMA, it is complicated …
  IBVerbs: 600 LOC
  RCMA CM: 300 LOC
  Rsocket: 60 LOC

## Slide 43: RDMA Programming
Make RDMA programming more accessible
  Easy-to-setup RDMA server and switch configurations
  Can I run and debug my RDMA code on my desktop/laptop?
  High quality code samples
Loosely coupled vs tightly coupled (Send/Recv vs Write/Read)

## Slide 44: Summary: RDMA for data centers!
RDMA is experiencing a renaissance in data centers
  RoCEv2 has been running safely in Microsoft data centers for two and half years
Many opportunities and interesting problems for high-speed, low-latency RDMA networking
Many opportunities in making RDMA accessible to more developers

## Slide 45: Acknowledgement
Yan Cai, Gang Cheng, Zhong Deng, Daniel Firestone, Juncheng Gu, Shuihai Hu, Hongqiang Liu, Marina Lipshteyn, Ali Monfared, Jitendra Padhye, Gaurav Soni, Haitao Wu, Jianxi Ye, Yibo Zhu
Azure, Bing, CNTK, Philly collaborators
Arista Networks, Cisco, Dell, Mellanox partners

## Slide 46: Questions?